## Slide 1
CLASS 2
IoT Architecture
& Interoperability
Smart Tags · IoT Hardware · Architecture Layers · Cloud Interoperability
Internet of Things | Undergraduate Course | AI Department
Book-1: Springer Handbook of IoT (Ziegler, 2024) | Book-2: Hands-On Industrial IoT (Veneri, 2024)

## Slide 2
Meeting 2 — Agenda
Smart tags: RFID, NFC, QR, and BLE beacons — identification at scale
IoT hardware: MCUs, SBCs, sensors, actuators, and prototyping platforms
IoT architecture: reference models, protocol stacks, and edge/fog/cloud
Interoperability in cloud IoT platforms: integration patterns and APIs
Lab: Wokwi simulation — ESP32 + DHT22 + MQTT (no physical hardware)
Q&A and recap

## Slide 3
01
Smart Tags: RFID, NFC, BLE Beacons
📚 Book-1, Ch.3-4, Pg 44-89

## Slide 4
Smart Tags: Auto-Identification Technologies
Smart tags = physical objects with embedded electronic identification capability
No keyboard input needed — data read wirelessly by scanners or smartphones
Core smart tag technologies:
  RFID (Radio Frequency Identification): radio waves identify tags passively or actively
  NFC (Near Field Communication): short-range (<4 cm) subset of RFID at 13.56 MHz
  BLE Beacons: Bluetooth Low Energy broadcasts short packets with ID and telemetry
  QR Codes: optical 2D barcodes — not wireless but ubiquitous for IoT device onboarding
  UWB (Ultra-Wideband): precise indoor positioning (<10 cm accuracy) via time-of-flight
Market size: smart tag market = USD 14.3B (2023) → USD 31.5B by 2030
Dominant use cases: retail inventory, supply chain, hospital asset tracking, contactless payment
Why they matter for IoT: smart tags are the bridge between physical objects and digital data systems
Every IoT deployment at scale (warehouse, hospital, factory) relies on smart tag identification
📚 Book-1, Ch.3-4, Pg 44-89

## Slide 5
RFID: Passive vs. Active vs. Semi-Passive
Passive RFID
Active RFID
Passive RFID:
No battery — powered by reader's RF field
Range: 0–10 cm (LF/HF) or 1–12 m (UHF)
LF (125 kHz): animal microchips, key fobs
HF (13.56 MHz = NFC): contactless payment, library books
UHF (860–960 MHz): retail tags, pallet tracking
Cost: $0.05–$0.25 per tag (UHF Gen2)
Standard: EPC Gen2 / ISO 18000-63
Example: Walmart's 1 billion RFID tags/year for retail inventory
Active & Semi-Passive RFID:
Active: onboard battery, continuous broadcast
Range: 20–100 m — tracks vehicles, trailers, containers
Semi-passive: battery for computation, RF-powered for transmission
Active RTLS (Real-Time Location Systems): AeroScout, Zebra
Use cases: hospital patient tracking, airport baggage, mining equipment
Active tag cost: $5–$25 (reusable, 3–5 year battery life)
Protocols: ISO 24730, IEEE 802.11 (Wi-Fi RTLS), UWB (IEEE 802.15.4a)
Example: GE Healthcare tracks 17,000 medical devices across hospital
📚 Book-1, Ch.3-4, Pg 44-89

## Slide 6
NFC: Near Field Communication in Detail
NFC = ISO 18000-3 (13.56 MHz), range < 4 cm, data rate 106/212/424 kbps
Derived from RFID but optimized for interactive use (tap-to-pair, tap-to-pay)
Three NFC operating modes:
  Reader/Writer: smartphone reads NFC tag (URL, vCard, Wi-Fi credentials on sticker)
  Card emulation: phone acts as RFID card — Apple Pay, Google Pay, transit cards
  Peer-to-peer (P2P): two NFC devices exchange data — Android Beam / Handover
NFC tag types (ISO/IEC 14443 Type A/B, ISO 15693):
  Type 1/2: NTAG213/216 (888 bytes) — cheapest, most deployed for smart posters, URL tags
  Type 4: MIFARE DESFire — encrypted, secure, used in contactless payment and ID cards
IoT applications of NFC:
  Device onboarding: tap phone to IoT device to transfer Wi-Fi credentials (WPS replacement)
  Product authentication: luxury goods, pharmaceuticals (tap to verify on blockchain)
  Maintenance logs: NFC tag on equipment stores last-service date, readable without internet
Global NFC adoption: 2.2 billion NFC-enabled phones worldwide (2024)
📚 Book-1, Ch.3-4, Pg 44-89

## Slide 7
BLE Beacons: Bluetooth Indoor Positioning
BLE Beacon = BT 4.0+ device that continuously advertises a short packet (no pairing required)
Three beacon protocols in use:
  iBeacon (Apple, 2013): broadcasts 128-bit UUID + Major + Minor ID; iPhone measures RSSI → proximity
  Eddystone (Google, 2015): three frame types — URL (physical web), UID (namespace+instance), TLM (telemetry)
  AltBeacon (Radius Networks, open source): hardware-vendor neutral alternative
Typical specs: 10m–70m range, coin-cell battery (1–3 years), update interval 100ms–10s
Proximity zones: Immediate (<0.5m), Near (0.5–3m), Far (3–30m), Unknown (signal too weak)
BLE 5.0 improvements (2016): 2× speed, 4× range, 8× broadcast capacity; Bluetooth Mesh added
Key IoT applications:
  Retail: notify app when customer near product (location-based push notification)
  Museum audio tours: exhibit triggers audio when visitor approaches
  Indoor navigation: airport/hospital wayfinding to <3m accuracy
  Asset tracking: Tile-style trackers on equipment, locating via nearby phones' Bluetooth scans
Apple AirTag / Samsung SmartTag: consumer BLE beacons using crowd-sourced network for tracking
📚 Book-1, Ch.3-4, Pg 44-89

## Slide 8
02
IoT Hardware: MCUs, SBCs, Sensors, Actuators
📚 Book-1, Ch.3-4, Pg 44-89

## Slide 9
Microcontrollers (MCU) vs. Single-Board Computers (SBC)
MCU: microcontroller unit — CPU + RAM + Flash + I/O on a single chip, runs firmware
  No OS (or bare-metal RTOS) — runs one program continuously
  Ultra-low power: 10 µA sleep mode, wake on interrupt — runs months on AAA battery
  Examples: ATmega328P (Arduino Uno), ESP32 (Wi-Fi+BLE+dual-core 240MHz), STM32, nRF52840
  Interfaces: GPIO, UART, SPI, I²C, ADC, PWM, USB, CAN — connect directly to sensors
SBC: single-board computer — full Linux/Windows OS, more powerful, more power-hungry
  Examples: Raspberry Pi 4 (4-core Cortex-A72, 4GB RAM, USB, HDMI, Ethernet, Wi-Fi)
  Runs Python, Node.js, Docker — acts as IoT gateway or local ML inference device
  Draws 3–7W continuously — needs reliable power supply (not battery-friendly)
Decision guide:
  Use MCU: battery-powered sensor nodes, <1 KB data/cycle, latency-critical, cost <$5
  Use SBC: local gateway, camera/vision, ML inference, protocol bridging, cost $35–$80
Trend: System-on-Module (SoM) bridges the gap — ESP32-S3 has 8MB RAM + vector instructions for TinyML
📚 Book-1, Ch.3-4, Pg 44-89

## Slide 10
Essential IoT Hardware Components
ESP32 (Espressif)
Dual-core 240 MHz Xtensa LX6, 520KB RAM, Wi-Fi 802.11 b/g/n + BLE 4.2/5.0. Most popular IoT MCU worldwide. $3–8. Supported in Wokwi simulator.
Raspberry Pi 4B
ARM Cortex-A72 quad-core 1.8GHz, 1–8GB LPDDR4, Gigabit Ethernet, USB 3.0, 40-pin GPIO. Ideal IoT gateway. Runs full Linux + Python.
Arduino MKR GSM 1400
SAMD21 + u-blox SARA-G350 cellular modem. 4G LTE-M / NB-IoT connectivity built-in. IoT deployments where Wi-Fi not available.
Nordic nRF52840
Cortex-M4F 64MHz + 1MB Flash + 256KB RAM + BLE 5.0 + Thread + Zigbee + USB. Ultra-low-power mesh networking MCU. 1.8–3.6V supply.
DHT22 Sensor
Digital temperature (−40–80°C ±0.5°C) + humidity (0–100% ±2%) sensor. Single-wire protocol. 2.5 mA active. The most common IoT lab sensor.
MAX17048 Fuel Gauge
I²C battery state-of-charge IC. Reports battery % and voltage. Essential for battery-powered IoT nodes needing power management.
📚 Book-1, Ch.3-4, Pg 44-89

## Slide 11
Sensors: The Perception Layer in Detail
Sensor = transducer converting a physical quantity into an electrical signal
Primary sensor categories:
  Environmental: temperature (NTC thermistor, DHT22, DS18B20), humidity (capacitive), pressure (BMP280), CO₂ (SCD41 NDIR)
  Motion & Position: accelerometer (MPU-6050 6-DoF IMU), PIR (passive infrared), radar (24GHz mmWave)
  Optical: photodiode, LDR, OPT3001 ambient light, MLX90614 IR thermometer, camera (OV5640 5MP)
  Chemical: MQ-2 (LPG/smoke), MQ-135 (air quality), pH probe (analog), dissolved oxygen sensor
  Acoustic: MEMS microphone (SPH0645), ultrasonic rangefinder HC-SR04, piezoelectric vibration
Sensor specifications that matter for IoT design:
  Sensitivity: smallest detectable change (e.g., ±0.5°C resolution)
  Accuracy: systematic error vs. true value; need calibration against reference
  Range: min/max measurable values without saturation
  Interface: analog (needs ADC), digital (I²C, SPI, UART) — digital preferred for noise immunity
  Power: crucial for battery devices — choose low active current + deep sleep mode
Sensor fusion: combining multiple sensors (accelerometer + gyroscope + magnetometer) via Kalman filter for robust positioning
📚 Book-1, Ch.3-4, Pg 44-89

## Slide 12
Actuators: Closing the IoT Control Loop
Actuator = device converting electrical signal into physical action
Why actuators matter: without actuators, IoT is passive monitoring; with them, it becomes control
Types of actuators in IoT:
  Electrical: relay module (switch 240VAC loads), MOSFET (PWM LED/motor control), solenoid valve (water control)
  Mechanical: stepper motor (3D printers, valve positioning, blinds), servo motor (angle control 0–180°), DC motor + H-bridge
  Thermal: Peltier module (precision temperature control), resistive heater element
  Display: SSD1306 OLED (I²C, 0.96"), TFT ILI9341, e-Paper (low power, retains image without power)
  Acoustic: piezo buzzer (alert tones), speaker (I²S DAC for voice output)
PWM (Pulse Width Modulation): key MCU technique for analog-like output from digital GPIO
  50Hz signal, duty cycle 0–100% controls LED brightness, motor speed, servo angle
  ESP32 has 16 independent LEDC PWM channels at up to 40 MHz
Safety consideration: relay module switches mains voltage — optocoupler isolation required between MCU and relay coil
Industry 4.0 actuator: servo-actuated proportional control valve with 4–20 mA current loop interface
📚 Book-1, Ch.3-4, Pg 44-89

## Slide 13
03
IoT Architecture: Layers, Models & Protocol Stacks
📚 Book-1, Ch.5-6, Pg 94-126

## Slide 14
IoT Reference Architecture Models
Multiple reference architectures exist — all describe the same system with different abstractions
IoT-A (EU FP7 Project) Reference Architecture: most comprehensive academic model
  D1 Perception: physical sensors, actuators, RFID, embedded MCUs
  D2 Network: connectivity, transport, routing (Wi-Fi, BLE, LoRa, Ethernet)
  D3 Service: middleware, device management, data storage, event processing
  D4 Application: user-facing apps, dashboards, APIs, business logic
  D5 Business: value model, data monetization, regulatory compliance
FIWARE Architecture (EU Horizon, open source):
  Generic Enablers: Orion Context Broker (NGSI-LD standard), IoT Agent, QuantumLeap TSDB
oneM2M Layered Architecture (global M2M standard):
  Three logical entities: Application Entity (AE), Common Services Entity (CSE), Network Services Entity (NSE)
  CSE provides 12 standard services: Device Management, Discovery, Location, Security, Analytics, etc.
AWS IoT Reference Architecture: Device Fleet → AWS IoT Core → Rules Engine → Analytics → DynamoDB → Lambda
Key principle: each layer is independently scalable and replaceable — this is the power of layered architecture
📚 Book-1, Ch.5-6, Pg 94-126

## Slide 15
Three-Tier IoT Architecture: Edge · Fog · Cloud
1
Edge Tier
Sensors and actuators. On-device MCU processing. BLE/Zigbee/LoRa local comms. Sub-millisecond response. <1MB RAM budget for TinyML.
2
Fog Tier
Local gateway / edge server (Raspberry Pi, industrial PC). MQTT broker. Local rule engine. Protocol translation. Caches data if cloud unreachable.
3
Cloud Tier
IoT platform (AWS IoT Core, Azure IoT Hub). Device registry for millions of devices. Time-series DB. Stream analytics. ML training pipeline.
4
Application Tier
Web/mobile dashboards. REST/GraphQL APIs. Digital twin visualization. Business intelligence. ERP/MES integration via APIs.
📚 Book-1, Ch.5-6, Pg 94-126

## Slide 16
IoT Protocol Stack: From Physical to Application
Physical Layer: electromagnetic signal transmission
  Radio: 2.4GHz (Wi-Fi/BLE/Zigbee), 868/915MHz (LoRa/Z-Wave), 700–900MHz (NB-IoT/LTE-M)
  Wired: RS-485 Modbus (industrial), Ethernet 802.3, CAN bus (automotive/industrial)
Data Link Layer: frame format, addressing, MAC access control
  IEEE 802.15.4: MAC layer for Zigbee, Thread, 6LoWPAN — CSMA-CA collision avoidance
  IEEE 802.11: Wi-Fi MAC — CSMA/CA + RTS/CTS, power save polling for IoT
Network Layer: addressing and routing
  IPv6: 128-bit addresses — the solution to IoT device address exhaustion (IPv4 can't scale to 29B devices)
  6LoWPAN: adapts IPv6 over 802.15.4 (compresses 40-byte IPv6 header to 8 bytes)
Transport Layer: reliable delivery
  TCP: reliable, ordered, connection-oriented — used where reliability > efficiency
  UDP: unreliable, fast — preferred by CoAP; allows multicasting to device groups
Application Layer: message format and semantics
  MQTT: publish/subscribe, QoS 0/1/2, 2-byte fixed header — optimal for constrained devices
  CoAP: REST-like (GET/PUT/POST/DELETE) over UDP — for MCUs with no TCP stack
  HTTP/REST + JSON: for gateway-to-cloud; too heavy for MCUs but standard for cloud APIs
  LwM2M: OMNA/OMA standard built on CoAP — device management protocol (OTA updates, config)
📚 Book-1, Ch.5-6, Pg 94-126

## Slide 17
MQTT Deep Dive: The Lingua Franca of IoT
MQTT (Message Queuing Telemetry Transport): publish/subscribe messaging protocol
Designed by IBM's Andy Stanford-Clark + Arcom's Arlen Nipper (1999) for oil pipeline telemetry
Standardized by OASIS (2013) — MQTT 3.1.1 (2014), MQTT 5.0 (2019)
Key design principles: minimal overhead, async messaging, reliable delivery on lossy networks
Architecture: clients publish to topics, broker routes to all subscribers
  Broker examples: Eclipse Mosquitto (open-source), HiveMQ (enterprise), AWS IoT Core, EMQX
Topic structure: hierarchical, slash-separated — e.g., 'factory/line1/machine3/temperature'
  Wildcards: '+' (single level) — 'factory/+/machine3/temperature' matches any line
  Wildcards: '#' (multi-level) — 'factory/#' matches everything under factory
Quality of Service (QoS) levels:
  QoS 0: at most once (fire and forget) — fastest, may lose messages
  QoS 1: at least once (acknowledged) — may duplicate, but guaranteed delivery
  QoS 2: exactly once (four-way handshake) — slowest, no duplicates, banking/medical
MQTT 5.0 additions: message expiry, user properties, subscription identifiers, shared subscriptions
Last Will and Testament (LWT): broker publishes offline alert if device disconnects abnormally
📚 Book-1, Ch.5-6, Pg 94-126

## Slide 18
04
Interoperability in Cloud IoT Platforms
📚 Book-1, Ch.5-6, Pg 94-126

## Slide 19
The Interoperability Challenge in IoT
Interoperability = the ability of different IoT systems to exchange and use information
Current state: severe fragmentation — 500+ IoT platforms, 100+ protocols, 1000s of device types
Levels of interoperability (IEEE definition):
  Technical interoperability: physical/logical connection (can data be transmitted?)
  Syntactic interoperability: same data format (can the data be parsed? JSON vs XML vs Protobuf)
  Semantic interoperability: same meaning (does 'temperature' in system A mean the same as in system B?)
  Organizational interoperability: business processes and governance aligned across organizations
Why semantic interoperability is hardest:
  'temperature' in weather IoT = ambient air; in manufacturing IoT = machine coolant; in medical IoT = body temp
  Without shared semantics, AI models trained on one system fail when deployed on another
Cost of poor interoperability: McKinsey estimates 40% of IoT value is locked behind integration friction
Solutions being deployed: oneM2M (horizontal platform), W3C WoT Thing Descriptions, FIWARE NGSI-LD, Matter
Key insight: interoperability is the #1 barrier to IoT at scale — solving it unlocks the $1.3T market
📚 Book-1, Ch.5-6, Pg 94-126

## Slide 20
Major Cloud IoT Platforms: Comparison
AWS IoT Core:
  Fleet size: 100M+ registered devices per account; 1B messages/day throughput
  Key services: IoT Core (MQTT/HTTPS broker), Greengrass (edge), SiteWise (industrial), TwinMaker
  Strengths: deepest AWS service integration, Lambda rules engine, SageMaker ML pipeline
Microsoft Azure IoT Hub:
  Supports MQTT, AMQP, HTTPS; device-to-cloud + cloud-to-device messaging
  Digital Twins service: graph-based live environment model, DTDL (Digital Twin Definition Language)
  Strengths: enterprise Windows/Active Directory integration, Time Series Insights, Azure ML
Google Cloud IoT Core (discontinued 2023 → Clearblade IoT Core):
  Lesson learned: even Google failed at IoT platform — market consolidating
Platform selection criteria: existing cloud vendor, required ML services, edge computing needs, pricing model
Data format for cross-platform: NGSI-LD (JSON-LD + semantic web) is emerging as the standard for semantic IoT data exchange between EU platforms (FIWARE-based)
📚 Book-1, Ch.5-6, Pg 94-126

## Slide 21
IoT Integration Patterns: How Systems Connect
Pattern 1 — Direct Device-to-Cloud (D2C):
  Device publishes directly to AWS IoT Core or Azure IoT Hub via MQTT over TLS
  Use when: device has 4G/Wi-Fi and enough processing power for TLS
  Advantage: simplest architecture; disadvantage: no local fallback if internet drops
Pattern 2 — Hub-and-Spoke via Gateway:
  Edge gateway (Raspberry Pi) collects BLE/Zigbee devices locally, forwards to cloud
  Use when: devices are low-power and cannot handle cloud TLS directly
  Advantage: local processing + store-and-forward when offline
Pattern 3 — Event-Driven via Message Queue:
  IoT device → MQTT broker → Apache Kafka → microservices (Node-RED, Lambda)
  Use when: many consumers need the same data (analytics + alerting + digital twin + storage simultaneously)
Pattern 4 — Peer-to-Peer (Matter/Thread):
  Devices communicate directly without cloud — local control, privacy-preserving
  Use when: smart home / building; cloud dependency unacceptable for latency or privacy
Pattern 5 — REST Pull (polling):
  Cloud API polls device for data on schedule — least efficient but simple to implement for monitoring dashboards
📚 Book-1, Ch.5-6, Pg 94-126

## Slide 22
Protocol Deep-Dive: MQTT vs. CoAP vs. HTTP
MQTT
CoAP
MQTT (pub/sub):
Transport: TCP (QoS 0/1/2)
Header: 2 bytes fixed + variable
Message size: no limit (configurable)
Pattern: publish/subscribe async
Broker needed: yes
QoS: 3 levels (0/1/2)
Security: TLS 1.2/1.3
Best for: telemetry, alerts, commands
Broker: Mosquitto, HiveMQ, AWS IoT Core
CoAP (request/response):
Transport: UDP (with optional DTLS)
Header: 4 bytes fixed
Message size: <1024 bytes typical
Pattern: REST-like (GET/PUT/POST/DELETE)
No broker needed: direct device-to-device
QoS: Confirmable (ACK) or Non-confirmable
Security: DTLS (UDP equivalent of TLS)
Best for: constrained devices, resource access
Proxy: CoAP-to-HTTP proxy for cloud integration
📚 Book-1, Ch.5-6, Pg 94-126

## Slide 23
W3C Web of Things (WoT): Semantic Interoperability
W3C WoT Working Group (2019): semantic layer to make IoT interoperable via web standards
Core concept: Thing Description (TD) — machine-readable JSON-LD document describing an IoT device
TD contains:
  Properties: readable state (e.g., 'temperature' with unit, data type, observable flag)
  Actions: invokable operations (e.g., 'setSetpoint' with input schema)
  Events: async notifications (e.g., 'overheat' event with threshold)
  Forms: protocol bindings — how to access each property via MQTT, CoAP, or HTTP
Key benefit: same client code can control any WoT-compliant device regardless of underlying protocol
Example TD use case: 'Find all temperature sensors in Building A with range 0–100°C' — discoverable via WoT Directory
Implementations: node-wot (Node.js), Eclipse ThingWeb, Siemens (contributed core WoT library)
Relationship to other standards:
  WoT TDs can wrap existing MQTT/HTTP/CoAP APIs without changing device firmware
  WoT Discovery uses IETF CoRE Resource Directory and DNS-SD for local device discovery
ETSI ISG CIM: NGSI-LD standard uses JSON-LD (same as WoT TD) for context broker queries — convergence happening
📚 Book-1, Ch.5-6, Pg 94-126

## Slide 24
LAB
Lab Session 2
📚 Wokwi Browser Simulator — No hardware required

## Slide 25
LAB
Lab 2: ESP32 + DHT22 on Wokwi + MQTT to HiveMQ
Tool: Wokwi.com (browser) + paho-mqtt Python or HiveMQ WebSocket client
Step 1 — Open Wokwi template:
→ Go to wokwi.com → New Project → ESP32 template
→ Add DHT22 sensor from component library (drag and drop)
→ Wire: DHT22 DATA → GPIO 15, VCC → 3.3V, GND → GND
Step 2 — Write firmware:
→ Include: WiFi.h, PubSubClient.h, DHT.h
→ Connect to Wokwi's virtual Wi-Fi (SSID: 'Wokwi-GUEST', password: '')
→ MQTT broker: broker.hivemq.com:1883
→ Loop: read DHT22 → format JSON → publish to 'wokwi/iot/dht22'
Step 3 — Subscribe and verify
→ On your laptop: python3 -c 'import paho.mqtt.client as m; ...' to subscribe
→ OR use HiveMQ Web Client at hivemq.com/demos/websocket-client/
Step 4 — Add control flow
→ Modify firmware: subscribe to 'wokwi/iot/led/control'
→ When 'ON' received, light simulated LED; when 'OFF', turn off
Submission: Wokwi project URL (shareable link) + screenshot of MQTT messages
Tool: Wokwi.com — free in-browser ESP32 / Arduino simulator (no account needed)
Goal: simulate a temperature/humidity IoT node publishing to a public MQTT broker

## Slide 26
Lab 2 Wokwi Firmware: ESP32 + DHT22 → MQTT
C++ (Arduino/ESP-IDF)
#include <WiFi.h>
#include <PubSubClient.h>
#include <DHT.h>
#define DHTPIN 15
#define DHTTYPE DHT22
DHT dht(DHTPIN, DHTTYPE);
const char* ssid = "Wokwi-GUEST";
const char* pass = "";
const char* broker = "broker.hivemq.com";
const char* topic = "wokwi/iot/dht22";
WiFiClient wifi; PubSubClient mqtt(wifi);
void setup() {
Serial.begin(115200); dht.begin();
WiFi.begin(ssid, pass);
while (WiFi.status() != WL_CONNECTED) delay(500);
mqtt.setServer(broker, 1883);
mqtt.connect("wokwi-esp32");
}
void loop() {
float t = dht.readTemperature();
float h = dht.readHumidity();
char buf[80];
snprintf(buf, 80, '{"temp":%.1f,"hum":%.1f}', t, h);
mqtt.publish(topic, buf);
delay(2000);
}

## Slide 27
Class 2 Recap
Key Takeaways
Smart tags (RFID, NFC, BLE) provide scalable physical-world identification without manual data entry
Passive UHF RFID ($0.05/tag) dominates supply chain; Active RFID/UWB enables real-time asset tracking
NFC = 13.56 MHz, <4 cm range; used for contactless payment, device onboarding, and authentication
MCU (ESP32, nRF52840): low-power sensor nodes; SBC (Raspberry Pi): gateway and local inference
IoT protocol stack: IEEE 802.15.4 → 6LoWPAN → IPv6 → UDP → CoAP (or TCP → MQTT) at application layer
MQTT: pub/sub over TCP, 2-byte header, QoS 0/1/2; the standard messaging protocol for IoT telemetry
Three-tier architecture: Edge (MCU+sensors) → Fog (gateway+local processing) → Cloud (platform+AI)
Interoperability levels: technical → syntactic → semantic → organizational; semantic is hardest and most valuable
W3C WoT Thing Descriptions: JSON-LD metadata enabling cross-platform discovery and unified API access
Lab: Wokwi ESP32 simulator publishes DHT22 data via MQTT to HiveMQ — complete IoT pipeline in browser
Book-1: Springer Handbook of IoT (Ziegler, 2024) | Book-2: Hands-On Industrial IoT (Veneri, 2024)