## Slide 1
CLASS 4
IoT Security & Privacy
Threats · Risk Assessment · Secure Communications · Authentication, Authorization & Accounting
Internet of Things | Undergraduate Course | AI Department
Book-1: Springer Handbook of IoT (Ziegler, 2024) | Book-2: Hands-On Industrial IoT (Veneri, 2024)

## Slide 2
Meeting 4 — Agenda
1. IoT security landscape: threat taxonomy and real-world incidents
2. Risk assessment for IoT systems: STRIDE, TARA, and threat modeling
3. Secure communications: TLS, DTLS, certificate management at scale
4. AAA framework: authentication, authorization, and accounting for IoT
5. Privacy by design in IoT: GDPR, data minimization, differential privacy
6. Lab: Python TLS-secured MQTT + JWT authentication (no hardware required)

## Slide 3
01
IoT Security Threats
📚 Book-1, Ch.11, Pg 210-243

## Slide 4
Why IoT Security is Uniquely Challenging
IoT devices are the weakest link in organizational security — but they connect to critical infrastructure
Unique security challenges vs. traditional IT:
  Constrained hardware: no OS-level security features, no TPM, no hardware RNG on $2 MCUs
  Long lifetimes: industrial sensors deployed for 10–20 years — outlive software support cycles
  Physical exposure: sensors on exterior walls, bridges, fields — anyone can physically access them
  Heterogeneous ecosystem: 500+ vendors, no common security baseline, no patching discipline
  Headless operation: no screen/keyboard for user to notice attack indicators
  Scale: attacking one vulnerability can be automated across millions of identical devices simultaneously
Consequence severity is high — IoT attacks affect physical world:
  Factory: compromised PLC → conveyor belt overspeed → mechanical damage + worker injury
  Smart building: thermostat hack → HVAC failure in server room → data center outage
  Medical: infusion pump hack → incorrect drug dosage → patient harm
  Water treatment: manipulated pH levels → public health emergency (Oldsmar, Florida 2021)
Verizon 2024 Data Breach Report: IoT devices involved in 13% of all breaches — up from 5% in 2020
📚 Book-1, Ch.11, Pg 210-243

## Slide 5
IoT Threat Taxonomy: OWASP IoT Top 10 (2018, updated 2023)
OWASP IoT Top 10 — the industry reference for IoT vulnerability categories:
T1 — Weak, guessable, or hardcoded passwords:
  Mirai botnet (2016): scanned internet for Telnet/SSH with 62 default credential pairs → compromised 600K cameras
  DDoS against Dyn DNS → took down Twitter, Netflix, Reddit for 6 hours
T2 — Insecure network services:
  Open Telnet (port 23), unencrypted HTTP admin panels, unnecessary open ports
T3 — Insecure ecosystem interfaces:
  Cloud API with no rate limiting or input validation; mobile app with cleartext token storage
T4 — Lack of secure update mechanisms:
  No OTA update → vulnerabilities persist forever; unsigned updates → attacker pushes malware
T5 — Use of insecure or outdated components:
  Embedded OpenSSL 1.0.1 (EOL 2020) with Heartbleed still running on IP cameras in 2024
T6 — Insufficient privacy protection: sending PII in cleartext; retaining data longer than needed
T7 — Insecure data transfer and storage: no TLS on MQTT; SQLite DB with no encryption on gateway
T8 — Lack of device management: no remote wipe, no device decommissioning process
T9 — Insecure default settings: Wi-Fi AP mode open by default; debug serial UART always enabled
T10 — Lack of physical hardening: JTAG/UART debug ports exposed; flash memory readable via SPI
📚 Book-1, Ch.11, Pg 210-243

## Slide 6
Notable IoT Security Incidents: Lessons Learned
Mirai Botnet (2016) — the defining IoT security event:
  Attack: automated scanner found 600,000 consumer cameras/routers with default credentials
  Method: Telnet brute-force with 62 manufacturer default username/password pairs
  Impact: 1.2 Tbps DDoS → Dyn DNS outage → half the US internet unreachable for 6 hours
  Lesson: default credentials must be banned; each device needs unique password from factory
Triton/TRISIS Industrial Attack (2017):
  Target: Schneider Electric Triconex Safety Instrumented System (SIS) at Saudi petrochemical plant
  Method: spear-phishing → IT network → pivot to OT network → malware targeted SIS PLCs
  Intent: disable safety shutdown systems → enable catastrophic physical explosion
  Lesson: IT/OT network segmentation is critical; safety systems must be air-gapped
Verkada Camera Breach (2021):
  150,000 Verkada security cameras accessed by hackers including hospital ICUs, Tesla factory, jails
  Root cause: super-admin credentials found in exposed Jenkins server — gave access to all customers
  Lesson: cloud IoT platform admin credentials must be protected; minimal-privilege API keys required
Oldsmar Water Treatment (2021):
  Attacker used TeamViewer (remote desktop) to increase sodium hydroxide (lye) levels by 11,100%
  Prevented by alert operator who saw mouse cursor moving and reversed the change
  Lesson: critical infrastructure requires multi-person authorization for dangerous parameter changes
📚 Book-1, Ch.11, Pg 210-243

## Slide 7
IoT Attack Vectors: The Full Surface
Physical Attacks
Chip decapping, JTAG/UART debug access, power glitching attacks (Rowhammer), cold-boot attacks, firmware extraction via SPI flash reader. Mitigation: epoxy-potted boards, fuse JTAG after manufacturing.
Network Attacks
Man-in-the-Middle (MQTT without TLS), replay attacks (old sensor readings injected), DDoS (volume floods), DNS spoofing (redirect device to malicious broker). Mitigation: TLS 1.3, certificate pinning, rate limiting.
Firmware Attacks
Malicious OTA update (if no signing), firmware extraction + reverse engineering, buffer overflow in parsing code (Ripple20 — 19 vulnerabilities in Treck TCP/IP stack affecting 100M+ devices). Mitigation: secure boot, signed updates, SBOM.
Protocol Attacks
MQTT without auth = anyone can publish false data to your topics. Zigbee unencrypted beacons. BLE MITM pairing. Z-Wave downgrade attack. Mitigation: TLS on MQTT, Zigbee security level 5, BLE LE Secure Connections.
Side-Channel Attacks
Power analysis (observe MCU power consumption while processing AES key → extract key bits). Timing attacks on RSA. EM emission analysis. Mitigation: masking in crypto libraries, constant-time implementations, hardware AES.
Supply Chain Attacks
Compromised firmware at factory (SolarWinds-style for hardware). Counterfeit components. Backdoored BSP (board support package). Mitigation: SBOM (Software Bill of Materials), code signing, hardware attestation.
📚 Book-1, Ch.11, Pg 210-243

## Slide 8
02
Risk Assessment for IoT Systems
📚 Book-1, Ch.11, Pg 210-243

## Slide 9
STRIDE Threat Modeling for IoT
STRIDE: Microsoft's threat modeling framework — categorizes threats by type of violation
S — Spoofing: attacker pretends to be a legitimate device or user
  IoT example: rogue sensor publishes fake temperature readings; attacker impersonates edge gateway
  Countermeasure: mutual TLS (client certificates), device attestation, X.509 device identity
T — Tampering: attacker modifies data in transit or at rest
  IoT example: MQTT message modified in transit to change setpoint; InfluxDB records altered
  Countermeasure: TLS for transport integrity; HMAC for message integrity; encrypted storage
R — Repudiation: actor denies performing an action
  IoT example: malicious actuator command sent, operator denies responsibility
  Countermeasure: signed commands with device certificates; immutable audit log
I — Information Disclosure: unauthorized access to data
  IoT example: MQTT traffic sniffed on open broker; GPS location data leaked from fleet
  Countermeasure: TLS 1.3 encryption; private broker with ACLs; data minimization
D — Denial of Service: attacker makes system unavailable
  IoT example: MQTT broker flooded with publish messages; gateway CPU overwhelmed
  Countermeasure: rate limiting, connection throttling, ACL by topic, Kafka backpressure
E — Elevation of Privilege: attacker gains more access than authorized
  IoT example: device with read-only cert can publish to command topic; API key with full admin access
  Countermeasure: MQTT ACL (per-topic read/write permissions); OAuth scope enforcement
📚 Book-1, Ch.11, Pg 210-243

## Slide 10
TARA: Threat Analysis and Risk Assessment (ISO 21434 / UNECE WP.29)
TARA: structured automotive cybersecurity risk assessment — adopted for industrial IoT and smart vehicles
Originally from ISO/SAE 21434 (Road Vehicle Cybersecurity), now widely applied to IIoT
TARA methodology steps:
  Step 1 — Asset Identification: list all IoT components with value: firmware, keys, sensor data, actuation commands
  Step 2 — Threat Scenario Analysis: for each asset, enumerate possible attack scenarios (STRIDE helps)
  Step 3 — Impact Rating: rate cybersecurity impact on Safety (S), Operational (O), Financial (F), Privacy (P)
  Safety impact: S0 (none) → S3 (life-threatening); Operational: O0 → O3 (critical service loss)
  Step 4 — Attack Feasibility: rate how easy the attack is: elapsed time, expertise, resources, window of opportunity
  Step 5 — Risk Determination: Risk = Impact × Feasibility → Risk Level 1–5
  Step 6 — Risk Treatment: Accept / Avoid / Transfer / Mitigate — select security controls
Risk matrix example for MQTT broker:
  Asset: MQTT broker admin credentials | Threat: Spoofing (stolen credentials)
  Impact: S2 (loss of control), O3 (complete service loss) → high impact
  Feasibility: low expertise needed, credential stuffing is automated → high feasibility
  Risk Level: 5 (Critical) → Mitigation: MFA on admin, per-device certificates, audit log
ISO 27001:2022 Annex A: 93 controls organized in 4 domains — organizational, people, physical, technological
📚 Book-1, Ch.11, Pg 210-243

## Slide 11
ETSI EN 303 645: Consumer IoT Cybersecurity Standard
ETSI EN 303 645 (published 2020): the first dedicated cybersecurity standard for consumer IoT
Mandated by: EU Cyber Resilience Act (CRA, 2024) — binding for all IoT products sold in EU from 2027
UK implemented similar rules: PSTI Act 2022 — in force from April 2024
13 provisions of EN 303 645:
  No universal default passwords — each device must have unique password or no password (force setup)
  Implement a means to manage reports of vulnerabilities — public disclosure contact
  Keep software updated — OTA update capability, signed updates, update notification
  Securely store credentials and security-sensitive data — no cleartext keys in flash
  Communicate securely — TLS 1.2+ for all cloud communication; no self-signed certs for production
  Minimize exposed attack surface — disable unused services; close unused ports
  Ensure software integrity — secure boot chain; cryptographic verification of firmware
  Ensure personal data is protected — GDPR principles embedded in device design
  Make systems resilient to outages — fail-safe defaults when cloud is unreachable
  Examine system telemetry data — log monitoring capability
  11–13. Delete personal data; make installation easy and secure; validate input data
CE marking for IoT products: from CRA effective date, non-compliant IoT devices cannot be sold in EU
📚 Book-1, Ch.11, Pg 210-243

## Slide 12
03
Secure Communications for IoT
📚 Book-1, Ch.12, Pg 248-283

## Slide 13
TLS 1.3 for IoT: The Foundation of Secure MQTT
Transport Layer Security (TLS): cryptographic protocol providing authentication, integrity, confidentiality
TLS 1.3 (RFC 8446, 2018): current standard — mandatory minimum for new IoT deployments
TLS 1.3 improvements over TLS 1.2 critical for IoT:
  1-RTT handshake (vs. 2-RTT in 1.2): halves connection establishment time — vital for duty-cycled MCUs
  0-RTT resumption: reconnecting device sends data with first packet — no handshake delay on reconnect
  Forward secrecy mandated: all cipher suites use ephemeral keys (DHE/ECDHE) — compromised key doesn't expose past traffic
  Removed weak algorithms: no RSA key exchange, no CBC, no RC4, no MD5/SHA-1 in TLS 1.3
TLS cipher suites in TLS 1.3 (only 5, all strong):
  TLS_AES_128_GCM_SHA256 — fastest, recommended for IoT
  TLS_AES_256_GCM_SHA384 — higher security, more compute
  TLS_CHACHA20_POLY1305_SHA256 — software-efficient, good for MCUs without AES hardware acceleration
Certificate types for IoT:
  X.509 v3: standard PKI certificate; RSA-2048 or EC P-256 (smaller, faster for IoT)
  ECC (Elliptic Curve Cryptography): P-256 key = 256 bits vs. RSA-2048 = 2048 bits — 8× smaller, 10× faster
MQTT over TLS (MQTTS): port 8883 — standard for production IoT; never use port 1883 (cleartext) in production
📚 Book-1, Ch.12, Pg 248-283

## Slide 14
DTLS: TLS for UDP-Based Protocols (CoAP)
DTLS (Datagram TLS, RFC 6347): TLS adapted for UDP — used with CoAP for constrained IoT devices
Why DTLS needed: CoAP runs on UDP; TLS requires TCP — need equivalent security for UDP
DTLS differences from TLS:
  Adds explicit sequence numbers to handle UDP packet reordering
  Adds handshake retransmission timer — UDP drops packets, DTLS retries automatically
  No record layer sequence number protection — uses UDP port for multiplexing
DTLS 1.2 (RFC 6347): current widely deployed version; DTLS 1.3 (RFC 9147, 2022) brings TLS 1.3 improvements
DTLS handshake: 4 flights (ClientHello → ServerHello → Certificate → Finished) — takes ~400 ms on 868 MHz LoRa link
Optimization for IoT: DTLS Connection ID (RFC 9146) allows DTLS session to survive device IP change
  Critical for NB-IoT/eMTC devices that sleep and re-register with new IP — no full re-handshake needed
Pre-shared keys (PSK) mode: MCU uses PSK instead of certificates — eliminates certificate verification overhead
  PSK-TLS: 50 µJ per handshake vs. 3,000 µJ for RSA — orders of magnitude cheaper on battery
Implementation: mbed TLS (ARM, open-source), wolfSSL (designed for MCUs, 20 KB ROM), TinyCrypt
📚 Book-1, Ch.12, Pg 248-283

## Slide 15
IoT PKI: Certificate Lifecycle Management at Scale
PKI (Public Key Infrastructure): system for issuing, managing, and revoking X.509 certificates
IoT PKI challenges differ fundamentally from web PKI:
  Scale: 1 million devices each need unique certificate — automated issuance mandatory
  Longevity: device lifespan 10–20 years vs. web cert 90-day renewal — long-lived certs with revocation
  Constrained devices: certificate verification may require 500 ms on slow MCU — optimize algorithm choice
IoT PKI architecture:
  Root CA: offline, air-gapped, hardware HSM — signs Intermediate CA certificates only; keys never touch network
  Intermediate CA (Manufacturing CA): issues device certificates during factory provisioning
  Device certificate: unique per-device EC P-256 certificate, burned into flash at factory
  Operator CA: issues gateway/server certificates for TLS server endpoints
Certificate enrollment methods:
  EST (RFC 7030, Enrollment over Secure Transport): HTTP/TLS-based; used by industrial IoT
  SCEP (Simple Certificate Enrollment Protocol): older, Cisco-origin; widely deployed in enterprise IoT
  ACME (RFC 8555): Let's Encrypt protocol — automated, free for gateway/server certs
Certificate revocation: CRL (Certificate Revocation List) too large for MCUs → OCSP Stapling preferred
AWS IoT Core: managed IoT PKI — auto-creates device certs, handles rotation, supports Just-in-Time Registration (JITR)
📚 Book-1, Ch.12, Pg 248-283

## Slide 16
IoT Secure Boot Chain
1
ROM Bootloader
Immutable code in silicon ROM. Verifies Stage-1 bootloader hash (SHA-256). Cannot be modified — hardware root of trust.
2
Stage-1 Bootloader
Stored in protected flash. Verifies Stage-2 or OS kernel signature using RSA-2048 or EC P-256 public key.
3
Stage-2 / RTOS
Verified OS or RTOS boots. Mounts encrypted file system (AES-256-XTS). Verifies application image.
4
Application
Verified application firmware runs. Connects to cloud using provisioned X.509 device certificate via TLS 1.3.
5
Attestation
Device proves identity to cloud using device certificate + challenge-response. Cloud verifies chain to Root CA.
📚 Book-1, Ch.12, Pg 248-283

## Slide 17
04
Authentication, Authorization & Accounting (AAA)
📚 Book-1, Ch.12, Pg 248-283 | Book-2, Ch.5, Pg 123-146

## Slide 18
AAA Framework: The Three Pillars of IoT Access Control
AAA = Authentication + Authorization + Accounting — the complete access control framework
Originally from RADIUS (RFC 2865, 1997) for network access; adapted for IoT ecosystem
Authentication: WHO are you? (verify identity)
  Pre-shared key (PSK): shared secret between device and server — simple but doesn't scale
  X.509 certificate: device presents signed certificate — scalable, auditable, revocable
  JWT (JSON Web Token): signed token for stateless authentication — used in IoT REST APIs
  OAuth 2.0: delegation protocol — device gets access token without exposing long-term credentials
Authorization: WHAT are you allowed to do? (enforce permissions)
  MQTT ACL: per-client, per-topic read/write permissions (e.g., device can only publish to its own topic)
  RBAC (Role-Based Access Control): roles (admin, operator, sensor) with permission sets
  ABAC (Attribute-Based Access Control): policies combine device attributes (location, type, health) for fine-grained control
Accounting: WHAT did you do? (audit trail)
  Every device connection, publish, subscribe, and command logged with timestamp and certificate fingerprint
  Log shipped to SIEM (Security Information and Event Management) for anomaly detection
  Immutable log: append-only storage (WORM) or blockchain anchoring for forensic evidence
📚 Book-1, Ch.12, Pg 248-283

## Slide 19
OAuth 2.0 and OpenID Connect for IoT Devices
IoT devices need to call REST APIs (e.g., firmware update server, digital twin API) securely
OAuth 2.0 (RFC 6749): authorization framework — device gets time-limited access token, not long-term password
OAuth flows suitable for IoT:
  Client Credentials Flow: for device-to-service (no human login) — device uses client_id + client_secret → access token
  Device Authorization Flow (RFC 8628): for devices with limited input (smart TV, IoT display)
  Device shows code on screen; user enters code on separate phone/PC to authorize → device polls for token
JWT (JSON Web Token, RFC 7519): stateless token used as OAuth access token
  Header: {'alg': 'RS256', 'typ': 'JWT'} — signature algorithm
  Payload: {'sub': 'device-001', 'scope': 'telemetry:write', 'exp': 1735689600} — claims
  Signature: HMAC-SHA256 or RSA-256 over base64(header).base64(payload)
  IoT benefit: gateway validates JWT locally without calling auth server each time — offline-capable
MQTT OAuth integration: MQTT CONNECT packet carries JWT in password field; broker validates signature
AWS IoT: uses Signature Version 4 (SigV4) for REST API calls + X.509 for MQTT authentication
Token rotation: short-lived access tokens (15 min) + long-lived refresh tokens (30 days) — compromise is time-limited
📚 Book-1, Ch.12, Pg 248-283

## Slide 20
MQTT Security: ACLs, TLS, and Authentication Deep Dive
Unsecured MQTT: the #1 IoT security misconfiguration — millions of open MQTT brokers on Shodan
Shodan IoT search: 'port:1883' returns 50,000+ open MQTT brokers exposing industrial/medical data
MQTT security checklist for production:
  ✅ Enable TLS 1.3 on port 8883 — never use port 1883 (cleartext) in production
  ✅ Require client authentication: X.509 client cert OR username/password minimum
  ✅ Configure ACL: each device can only publish/subscribe to its own topic namespace
  ✅ Enable Last Will and Testament: broker auto-publishes 'offline' status on abnormal disconnect
  ✅ Set keepalive: detect dead connections within 1.5× keepalive interval (e.g., 60 s keepalive → 90 s detection)
  ✅ Limit connection rate: prevent brute-force by rate-limiting new connections per IP
Mosquitto broker ACL file example:
  user device-001 → topic read iot/device-001/commands → topic write iot/device-001/telemetry
  user admin-dashboard → topic readwrite iot/# → topic readwrite $SYS/#
HiveMQ Enterprise: RBAC with LDAP integration, audit logging, Kafka extension, TLS termination
AWS IoT Core policies: IAM-like JSON policies per certificate; topic patterns support ${iot:ClientId}
  Policy: 'iot:Publish' on 'iot/device/${iot:ClientId}/data' — each device can only publish to its own topic
📚 Book-1, Ch.12, Pg 248-283

## Slide 21
IoT Security: Defense-in-Depth
Hardware + Firmware
Network + Application
Layer 1 — Hardware Root of Trust:
ARM TrustZone: secure enclave on Cortex-M23/M33
ATECC608B: dedicated crypto co-processor with secure key storage
Secure Boot: ROM verifies every bootloader stage
PUF (Physical Unclonable Function): device fingerprint from silicon variation
Layer 2 — Firmware Security:
Signed OTA updates (Ed25519 signature)
SBOM (Software Bill of Materials): all libraries tracked
Stack canaries + ASLR on capable MCUs
Fuzz testing of all parser code (libFuzzer)
Layer 3 — Network Security:
TLS 1.3 on all cloud communications (port 8883)
Certificate pinning: reject unexpected server certs
Network segmentation: IoT VLAN separate from IT
Firewall: allow only outbound 8883 → broker
Layer 4 — Application Security:
MQTT ACL: per-device topic namespacing
OAuth 2.0 + short-lived JWT for API calls
Input validation: reject malformed JSON payloads
Layer 5 — Monitoring:
SIEM integration: ship all device logs to Splunk/Elastic
Anomaly detection: ML model on device behavior baseline
Incident response playbook: isolate → investigate → patch
📚 Book-1, Ch.12, Pg 248-283

## Slide 22
05
Privacy in IoT: GDPR, Data Minimization, Differential Privacy
📚 Book-2, Ch.5, Pg 123-146

## Slide 23
GDPR and IoT: Privacy Obligations for Device Makers
GDPR (EU General Data Protection Regulation, effective May 2018): applies to all IoT processing EU personal data
Personal data in IoT context: far broader than name/email:
  Location data (GPS coordinates, Wi-Fi triangulation) → identifies home, workplace, habits
  Biometric data (fingerprint scanner, face recognition camera, voice, gait) → GDPR Article 9, special category
  Health data (medical sensor readings: ECG, glucose, blood pressure) → special category, highest protection
  Behavioral data (smart meter usage patterns → inferring home occupancy, sleep patterns)
Key GDPR obligations for IoT manufacturers:
  Lawful basis: must have consent, legitimate interest, or contract to process IoT sensor data
  Purpose limitation: collected data cannot be used for a different purpose without new consent
  Data minimization: only collect the minimum data necessary for the stated purpose
  Storage limitation: delete data when no longer needed — no indefinite cloud storage
  Data subject rights: right to erasure ('right to be forgotten') — must delete from cloud + edge + backup
Article 25: Privacy by Design and by Default — privacy protections must be embedded in product architecture
Fines: up to €20M or 4% of global turnover — Amazon fined €746M in Luxembourg (2021)
IoT-specific guidance: EDPB Guidelines on connected vehicles, smart home, and wearable devices
📚 Book-2, Ch.5, Pg 123-146

## Slide 24
Privacy-Enhancing Technologies for IoT
Privacy by Design (PbD): 7 foundational principles for IoT product development
  1. Proactive not reactive — anticipate privacy risks before deploying
  2. Privacy as the default — maximum privacy settings out of the box; user opts in to share more
  3. Privacy embedded into design — not bolt-on compliance checkbox
  4. Full functionality — privacy and functionality are not a zero-sum trade-off
  5. End-to-end security — device-to-cloud TLS + at-rest encryption
  6. Visibility and transparency — open about what is collected and why
  7. Respect for user privacy — user-centric controls and data portability
Differential Privacy: mathematical framework to add controlled noise to data so individual cannot be identified
  Apple uses DP for keyboard usage statistics from 1 billion iPhones without learning any individual's typing
  Google RAPPOR: frequency estimation across Chrome users with (ε,δ)-differential privacy guarantee
  IoT application: smart building occupancy statistics shared with research without revealing who was there
K-anonymity: publish sensor data only when k≥10 devices share identical attribute values — no individual identifiable
Homomorphic encryption: compute on encrypted sensor data without decrypting — cloud never sees raw values
  Limited to simple operations today (sums, averages) — too compute-intensive for complex IoT ML
Federated Learning (see Week 3): the pragmatic privacy solution — train models without centralizing personal IoT data
📚 Book-2, Ch.5, Pg 123-146

## Slide 25
LAB
Lab Session 4
📚 Python TLS + JWT Authentication — No hardware required

## Slide 26
LAB
Lab 4: Secure MQTT with TLS + JWT Authentication
Tool: Python 3 + paho-mqtt + pyjwt + cryptography + HiveMQ Cloud (free) or local Mosquitto
Part 1 — TLS-secured MQTT:
→ Use HiveMQ Cloud (free tier at hivemq.com/mqtt-cloud/) — provides TLS endpoint automatically
→ Free cluster: uniqueID.s1.eu.hivemq.cloud:8883 (TLS) + username/password auth
→ Publisher (secure_publish.py):
client.tls_set(tls_version=ssl.PROTOCOL_TLS_CLIENT)
client.username_pw_set('your_username', 'your_password')
client.connect('uniqueID.s1.eu.hivemq.cloud', 8883, 60)
→ Verify: Wireshark capture should show TLS encrypted traffic (not readable MQTT)
Part 2 — JWT token generation and validation:
→ pip install pyjwt cryptography
→ Generate RS256 private/public key pair (openssl genrsa + openssl rsa -pubout)
→ Create JWT: jwt.encode({'device_id':'esp32-001','scope':'telemetry:write','exp':...}, key, 'RS256')
→ Validate JWT: jwt.decode(token, public_key, algorithms=['RS256'])
→ Simulate: publisher signs each MQTT message payload with JWT claim
→ Subscriber verifies JWT before accepting data — rejects expired/invalid tokens
Part 3 — Threat simulation:
→ Try connecting without TLS (port 1883) → should be rejected by HiveMQ Cloud
→ Try publishing with expired JWT → subscriber rejects with 'Token expired' error
→ Observe Mosquitto broker ACL: attempt to publish to a different device's topic → rejected
Goal: implement a production-grade secure MQTT connection with certificate-based TLS and JWT auth

## Slide 27
Lab 4 Code: TLS-Secured MQTT Publisher with JWT Payload Signing
Python
import ssl, json, time, jwt, datetime
import paho.mqtt.client as mqtt
# === Configuration ===
BROKER = 'uniqueID.s1.eu.hivemq.cloud’ # HiveMQ Cloud
PORT = 8883 # TLS port
USERNAME = 'iot_device'
PASSWORD = 'your_secure_password'
TOPIC = 'iot/secure/device001/telemetry'
# Load RSA private key for JWT signing
with open('device_private_key.pem', 'r') as f:
PRIVATE_KEY = f.read()
def make_jwt_payload(device_id, data):
return jwt.encode({
'device_id': device_id,
'scope': 'telemetry:write',
'data': data,
'iat': datetime.datetime.utcnow(),
'exp': datetime.datetime.utcnow() + datetime.timedelta(minutes=5)
}, PRIVATE_KEY, algorithm='RS256')
client = mqtt.Client(mqtt.CallbackAPIVersion.VERSION2)
client.tls_set(tls_version=ssl.PROTOCOL_TLS_CLIENT)
client.username_pw_set(USERNAME, PASSWORD)
client.connect(BROKER, PORT, 60)
while True:
payload = make_jwt_payload('device-001', {'temp': 22.5, 'hum': 65})
client.publish(TOPIC, payload)
time.sleep(5)

## Slide 28
Lab 4 Code: TLS-Secured MQTT Subscriber with JWT Verification
Python
import ssl, json, jwt
import paho.mqtt.client as mqtt
BROKER = 'uniqueID.s1.eu.hivemq.cloud'
PORT = 8883
USERNAME = 'iot_dashboard'
PASSWORD = 'your_secure_password'
TOPIC = 'iot/secure/device001/telemetry'
# Load RSA public key for JWT verification
with open('device_public_key.pem', 'r') as f:
PUBLIC_KEY = f.read()
def on_message(client, userdata, message):
try:
claims = jwt.decode(message.payload.decode(),
PUBLIC_KEY,
algorithms=['RS256'])
data = claims['data']
device = claims['device_id']
print(f'✅ Verified [{device}]: {data}')
except jwt.ExpiredSignatureError:
print('❌ Rejected: JWT expired')
except jwt.InvalidSignatureError:
print('❌ Rejected: invalid JWT signature')
client = mqtt.Client(mqtt.CallbackAPIVersion.VERSION2)
client.tls_set(tls_version=ssl.PROTOCOL_TLS_CLIENT)
client.username_pw_set(USERNAME, PASSWORD)
client.on_message = on_message
client.connect(BROKER, PORT, 60)
client.subscribe(TOPIC)
client.loop_forever()

## Slide 29
Course Wrap-Up: Key Takeaways Across 4 Meetings
Class 1 — IoT Foundations: IoT = smart objects + connectivity + intelligence. 29 billion devices by 2030. From telegraph (1832) to AI-powered edge devices today.
Class 2 — Architecture: RFID/NFC/BLE tags identify physical world. MQTT pub/sub is the universal IoT messaging protocol. Interoperability remains the key challenge.
Class 3 — Edge Intelligence: Process data near the source. TinyML enables on-device AI. Federated learning enables privacy-preserving model training across device fleets.
Class 4 — Security: IoT attacks have physical consequences. Defense-in-depth: secure boot → TLS 1.3 → MQTT ACLs → AAA → monitoring. Privacy is a design requirement, not an afterthought.
The big picture — why IoT matters for AI engineers:
  IoT is how AI reaches the physical world — without sensors and actuators, AI is just text and images
  Edge AI (TinyML) is the fastest-growing ML deployment environment — billions of inference endpoints
  Industrial IoT data is the highest-value ML training data — time-series sensor data for predictive maintenance
  Security and privacy are non-negotiable — compromised IoT = compromised physical infrastructure
Recommended next steps: AWS IoT Core free tier, Edge Impulse free account, Wokwi simulation, HiveMQ Cloud free
📚 Book-1, Ch.12, Pg 248-283 | Book-2, Ch.5, Pg 123-146

## Slide 30
Class 4 Recap
Key Takeaways
OWASP IoT Top 10: hardcoded passwords (#1), insecure network services (#2), missing OTA updates (#4) — know these cold
Mirai botnet (2016): 600K cameras with default credentials → 1.2 Tbps DDoS → half the US internet offline
STRIDE threat model: Spoofing/Tampering/Repudiation/Info Disclosure/DoS/Elevation — apply to every IoT design
ETSI EN 303 645: EU mandatory IoT security standard from 2027 — 13 provisions including no default passwords, signed OTA, TLS
TLS 1.3: 1-RTT handshake, forward secrecy mandatory, 5 strong cipher suites — use on port 8883 for MQTT
DTLS + PSK: UDP equivalent of TLS for CoAP; PSK mode uses 50 µJ vs. 3,000 µJ for RSA — battery-critical
AAA = Authentication (who?) + Authorization (what?) + Accounting (audit trail) — three inseparable pillars
OAuth 2.0 Client Credentials + short-lived JWT: stateless IoT API authentication without long-term credential exposure
GDPR for IoT: location, biometrics, health data are personal data — purpose limitation, minimization, erasure rights apply
Differential Privacy + Federated Learning: the two key mathematical tools for privacy-preserving IoT AI deployment
Book-1: Springer Handbook of IoT (Ziegler, 2024) | Book-2: Hands-On Industrial IoT (Veneri, 2024)