## Slide 1
CLASS 3
Edge Computing &
Distributed Intelligence
Edge Computing · Resource Management · Distributed Intelligence · AIoT at the Edge
Internet of Things | Undergraduate Course | AI Department
Book-1: Springer Handbook of IoT (Ziegler, 2024) | Book-2: Hands-On Industrial IoT (Veneri, 2024)

## Slide 2
Class 3 — Agenda
1. Edge computing fundamentals: why, what, and where
2. Resource management at the edge: compute, memory, energy budgets
3. Benefits and challenges of edge intelligence for IoT
4. Distributed intelligence: federated learning, swarm intelligence
5. Building IoT edge infrastructure: Node-RED + edge analytics
6. Lab: Node-RED edge pipeline — sensor data → local rules → dashboard

## Slide 3
01
Edge Computing Fundamentals
📚 Book-1, Ch.7, Pg 130-142

## Slide 4
Why Edge Computing? The Case Against Pure Cloud IoT
Problem 1 — Latency: cloud round-trip adds 50–200 ms; unacceptable for safety-critical control
  Autonomous vehicle: pedestrian detection requires <10 ms decision — cloud is physically impossible
  Industrial robot collision avoidance: 1 ms response window — must be on-device
  Remote surgery (haptic feedback): >20 ms feels like 'sticky' — operator loses precision
Problem 2 — Bandwidth: raw sensor data is enormous and expensive to transmit
  A single factory HD camera generates 3 Gbps of raw video
  100 cameras = 300 Gbps → impossible to stream to cloud continuously
  Solution: process at the edge, send only 'events' or 'anomaly flags' to cloud (1000× reduction)
Problem 3 — Reliability: cloud dependency creates single point of failure
  If internet goes down, cloud-only IoT system goes blind — edge keeps operating locally
Problem 4 — Privacy and compliance: data sovereignty laws prevent sending certain data to cloud
  GDPR Article 5(1)(e): personal data must not leave EU without adequate protection
  Industrial IP: machining parameters are trade secrets — cannot be sent to vendor's cloud
Conclusion: edge computing is not optional for production IoT — it is an architectural requirement
📚 Book-1, Ch.7, Pg 130-142

## Slide 5
Defining Edge Computing: Terminology and Topology
Edge computing: processing data near its source rather than centralizing in a remote cloud data center
The edge-fog-cloud continuum:
  On-device edge (Tier 0): MCU runs ML inference locally — ESP32-S3, STM32H7, Arduino Nicla Vision
  Near-edge (Tier 1): device-local gateway — Raspberry Pi 4, NVIDIA Jetson Nano, Intel NUC
  Far-edge (Tier 2): enterprise edge server at factory/hospital floor — Dell PowerEdge micro, HPE Edgeline
  Regional cloud (Tier 3): CSP regional data center (e.g., AWS us-east-1) — 5–50 ms latency
  Central cloud (Tier 4): global cloud backbone — training, archival, global analytics
Latency by tier: Tier 0 = <1 ms | Tier 1 = 1–10 ms | Tier 2 = 10–30 ms | Tier 3 = 30–100 ms | Tier 4 = 100–500 ms
Market: edge computing market USD 61.1B (2023) → USD 232.1B by 2030 (CAGR 21%)
Drivers: 5G rollout, AI democratization, Industry 4.0, autonomous vehicles, smart cities
📚 Book-1, Ch.7, Pg 130-142

## Slide 6
Edge Computing: Key Metrics
<10ms
Target Latency
Industrial control applications
1000×
Data Reduction
Edge processing vs. raw stream
$232B
Market by 2030
CAGR 21%, IDC forecast
📚 Book-1, Ch.7, Pg 130-142

## Slide 7
MEC: Multi-Access Edge Computing (ETSI Standard)
MEC standardized by ETSI ISG MEC (2014–present): edge computing at cellular base station
Architecture: MEC host co-located with 4G/5G base station → 1–10 ms from any mobile device
Key ETSI MEC concepts:
  MEC Platform: virtualization infrastructure at cell tower running MEC applications
  MEC App: containerized workload (e.g., video analytics, AR rendering) running at the tower
  UPF (User Plane Function): 5G network element that steers traffic to MEC host vs. internet
  Application mobility: MEC app can migrate between towers as device moves — session continuity
5G + MEC use cases enabled:
  AR/VR: game rendering at cell tower → headset receives only display output → untethered VR
  V2X (Vehicle-to-Everything): RSU (roadside unit) MEC processes all intersection sensor feeds → <5 ms
  Drone fleet: operator at MEC host sees drone video with <10 ms delay even at 4K resolution
Key standard: ETSI GS MEC 003 — API for MEC applications
Implementation: AWS Wavelength, Azure Edge Zones, Verizon 5G Edge are commercial MEC deployments
📚 Book-1, Ch.7, Pg 130-142

## Slide 8
02
Resource Management at the Edge
📚 Book-1, Ch.7, Pg 130-142

## Slide 9
The Edge Resource Constraint Triangle
Edge IoT devices must balance three competing constraints simultaneously:
Constraint 1 — Compute: MCUs have 240 MHz max (ESP32) vs. server CPUs at 3+ GHz
  Available for ML inference: 1–100 MOPS (million ops per second) on MCU vs. 100 TOPS on GPU
  Solution: quantize ML models to INT8 (8-bit integers) — 4× size reduction, 2× speed vs. FP32
Constraint 2 — Memory: MCUs have 256 KB – 8 MB RAM vs. servers with GBs
  An LSTM model for predictive maintenance with 128 units = 262 KB — barely fits in 512 KB RAM
  Solution: TinyML model compression — pruning, knowledge distillation, architecture search (MobileNet, EfficientNet-Lite)
Constraint 3 — Energy: battery-powered sensors have 1,000–10,000 mAh total
  ESP32 active mode (Wi-Fi on): 240 mA → 1000 mAh battery lasts ~4 hours
  ESP32 deep sleep: 10 µA → 1000 mAh battery lasts 11 years!
  Solution: duty cycling — wake every 15 min, read sensor, publish, go back to sleep
The golden rule of edge IoT: what you don't compute doesn't cost energy; sleep is free
Resource-aware design: choose algorithm complexity based on budget, not accuracy maximization
📚 Book-1, Ch.7, Pg 130-142

## Slide 10
Energy Harvesting: Zero-Battery IoT
Battery replacement is the biggest operational cost of large IoT deployments at scale
Example: 10,000 sensor nodes × battery replacement every 2 years = 5,000 battery swaps/year → prohibitive
Energy harvesting: capture ambient energy from environment to power IoT node indefinitely
Solar harvesting:
  Indoor (office light): 10–100 µW/cm² from fluorescent/LED lighting
  Outdoor direct sunlight: 10–15 mW/cm² with monocrystalline solar cell at 22% efficiency
  IC: SPV1040 (STMicro) MPPT solar charger + LTC3105 for very low illuminance
Thermal harvesting (TEG):
  Thermoelectric generator: Seebeck effect — 1 µW to 30 mW from industrial pipe temperature gradient
  Use case: wireless sensor on steam pipe (200°C) → ambient air (25°C) → 175°C ΔT → self-powered
RF energy harvesting:
  Ambient Wi-Fi/cellular radio waves → Powercast P21XXCSR-EVB rectenna → 10–100 µW at 1 m from AP
  Sufficient for BLE beacon or temperature reading every 30 seconds
Piezoelectric harvesting:
  Vibration from machinery → PZT ceramic → 10–1000 µW — self-powered vibration sensor on pump
Products: EnOcean self-powered switches (no battery, no wiring); Everactive batteryless BLE sensor for industrial monitoring
📚 Book-1, Ch.7, Pg 130-142

## Slide 11
Container Orchestration at the Edge: K3s and KubeEdge
Edge computing at scale requires managing 100s–1000s of edge nodes systematically
Kubernetes: the standard container orchestration platform (Google, 2014 → CNCF)
  Problem: full K8s requires 4 vCPU + 4 GB RAM — too heavy for edge nodes
K3s (Rancher/SUSE): lightweight Kubernetes for edge and IoT
  Binary size: 50 MB (vs. 200 MB for K8s); runs on Raspberry Pi 4 with 1 GB RAM
  Features: full K8s API compatibility + embedded SQLite DB (no etcd needed) + built-in Helm
  Use case: manage fleet of Raspberry Pi edge gateways from central K3s server
KubeEdge (CNCF): extends K8s to heterogeneous edge hardware
  EdgeCore: lightweight agent on edge device (runs on ARM MCUs with 64 MB RAM)
  CloudCore: K8s extension that manages EdgeCore agents remotely
  EdgeMesh: distributed service mesh for edge-to-edge communication
AWS IoT Greengrass v2: AWS-managed edge runtime
  Deploys Lambda functions and Docker containers to edge devices via IoT Core
  Component model: pre-built components for MQTT bridge, inference, stream manager
Azure IoT Edge: deploys Docker containers to edge from Azure IoT Hub + Azure ML edge deployment
📚 Book-1, Ch.7, Pg 130-142

## Slide 12
03
Benefits and Challenges of Edge Intelligence
📚 Book-2, Ch.4, Pg 100-111

## Slide 13
Benefits of Edge Intelligence
Ultra-Low Latency
On-device inference: 0.5–5 ms vs. 50–300 ms for cloud round-trip. Enables real-time control: motor, robotics, safety shutdown, autonomous navigation.
Bandwidth Savings
Raw camera: 3 Gbps. Edge YOLO inference sends only bounding box JSON: 1 KB/frame. 99.9% bandwidth reduction — makes dense sensor deployments feasible.
Offline Operation
Edge intelligence operates without internet. Factory floor, ship, remote mine, autonomous vehicle — none can tolerate cloud dependency for safety.
Privacy Preservation
Personal data (face, voice, health vitals) processed on-device, never leaves the edge. Compliant with GDPR, HIPAA, CCPA by design — no consent needed for local processing.
Cost Reduction
AWS IoT Core: $1/million messages. 1B messages/day × $1/1M = $1,000/day. Edge processing eliminates 99% of cloud messages → $10/day. Massive savings at scale.
Reliability
SLA: 99.99% uptime for cloud = 52 min downtime/year. For safety systems, even 1 minute is unacceptable. Edge operation provides local fallback always.
📚 Book-2, Ch.4, Pg 100-111

## Slide 14
Challenges of Edge Intelligence
Challenge 1 — Model accuracy vs. size tradeoff:
  MobileNetV3-Small: 2.5 MB, 67.4% ImageNet Top-1 accuracy vs. ResNet-50: 98 MB, 76.1%
  For many real-world tasks, 67% accuracy is insufficient — requires careful task-specific evaluation
Challenge 2 — Hardware diversity and fragmentation:
  100s of MCU architectures: ARM Cortex-M, RISC-V, Xtensa, AVR — no single binary runs everywhere
  Solution: TensorFlow Lite Micro, ONNX Runtime Mobile, Edge Impulse — provide cross-platform runtimes
Challenge 3 — Over-the-Air (OTA) model updates:
  Deployed model becomes stale as data distribution drifts — accuracy degrades silently
  Updating 10,000 devices with new model firmware: needs signed update, rollback mechanism, A/B partitioning
Challenge 4 — Security of edge devices:
  Physical access to edge device = potential to extract firmware, model weights, and sensor data
  Mitigation: ARM TrustZone, Secure Boot, encrypted model storage
Challenge 5 — Power management complexity:
  Duty cycling breaks TCP connections, MQTT sessions, TLS handshakes — need careful reconnect logic
  Edge Impulse study: incorrect sleep implementation can actually increase power 3× vs. no sleep
Challenge 6 — Debugging at the edge:
  No keyboard, no display — failures manifest as silent data gaps or wrong actuator states
  Solution: remote logging via MQTT, watchdog timers, heartbeat topics, anomaly-triggered log upload
📚 Book-2, Ch.4, Pg 100-111

## Slide 15
04
Distributed Intelligence at the Edge
📚 Book-1, Ch.7, Pg 130-142 | Book-2, Ch.4, Pg 100-111

## Slide 16
Federated Learning: AI Without Centralizing Data
Classic ML: collect all data in cloud → train model → deploy globally (privacy risk, bandwidth cost)
Federated Learning (Google, McMahan et al., 2017): train ML model across distributed edge devices without sharing raw data
Algorithm: Federated Averaging (FedAvg):
  Round 1: Server sends initial global model to all edge devices
  Round 2: Each device trains locally on its own data for N local steps
  Round 3: Devices send model gradient updates (not raw data) to server
  Round 4: Server aggregates gradients (weighted average) → new global model
  Repeat until convergence
Privacy guarantee: raw data never leaves the device — only gradient vectors are shared
IoT federated learning applications:
  Keyboard next-word prediction (Google Gboard): trained on 500M phones without ever seeing user text
  Industrial predictive maintenance: 100 factories share a vibration anomaly model without sharing proprietary process data
  Healthcare wearables: ECG arrhythmia detection model trained across hospitals without patient data leaving institution
Frameworks: TensorFlow Federated, PySyft (OpenMined), NVIDIA FLARE, Flower (flwr.ai)
Challenge: communication overhead, non-IID data distributions, adversarial clients (gradient poisoning)
📚 Book-1, Ch.7, Pg 130-142

## Slide 17
TinyML: Machine Learning on Microcontrollers
TinyML: ML inference on MCUs with <1 MB RAM and <1 mW power budget
Why TinyML matters: eliminates cloud dependency for AI — intelligence moves to the endpoint
Key techniques enabling TinyML:
  Quantization: convert FP32 weights → INT8 (4× smaller, 2–3× faster, <1% accuracy loss typically)
  Pruning: remove near-zero weights — structured pruning removes entire filters for hardware speedup
  Knowledge distillation: small 'student' model trained to mimic large 'teacher' model outputs
  Neural Architecture Search (NAS): AutoML-optimized architectures for constrained targets (MobileNet, EfficientNet, MCUNet)
Hardware enablers:
  ARM Cortex-M55: first Cortex-M with Helium SIMD vector extension — 15× ML performance vs. M4
  Ambiq Apollo4 Blue: Cortex-M4F with 1 mW AI inference — target for always-on keyword detection
  GAP9 (GreenWaves Technologies): RISC-V multi-core with CNN accelerator — 1 TOPS/W efficiency
Benchmark: MLPerf Tiny — standardized benchmarks for Keyword Spotting, Visual Wake Words, Anomaly Detection, Image Classification on MCUs
Tools: Edge Impulse (cloud-to-MCU ML pipeline), TensorFlow Lite Micro (TFLM), Arduino ML Tools
📚 Book-1, Ch.7, Pg 130-142

## Slide 18
Swarm Intelligence and Collective IoT Behaviour
Swarm intelligence: collective intelligence emerging from simple, decentralized, self-organizing agents
Biological inspiration: ant colonies (pheromone trails), bee swarms (waggle dance), bird flocking (Reynolds rules)
IoT swarm applications:
  Drone swarm search and rescue: 50 drones coordinate without central control; stigmergy-based search
  Agricultural robot swarm: 10 weed-pulling robots share crop map via BLE mesh, never overlap coverage
  Smart building HVAC: thousands of sensors vote on comfort setpoint — no central thermostat needed
Swarm algorithms:
  Ant Colony Optimization (ACO): pheromone-based distributed routing — IoT mesh path selection
  Particle Swarm Optimization (PSO): collective optimization — antenna array beamforming in 5G base stations
  Flocking (Boids): Reynolds 3 rules (separation, alignment, cohesion) → collision-free multi-robot motion
Stigmergy: indirect coordination via environment modification
  RFID tags on warehouse shelves = digital pheromone trails — robots modify and read shared state
Gossip protocols: each node randomly selects neighbor to share state — converges to global consensus in O(log N) rounds
  Application: distributed aggregation — 1000 temperature sensors compute global average without central server
📚 Book-2, Ch.4, Pg 100-111

## Slide 19
Edge AI Frameworks Comparison
TensorFlow Lite Micro
Edge Impulse
TensorFlow Lite Micro (TFLM):
Google/TensorFlow Foundation open-source
Runs on Cortex-M4/M7, ESP32, nRF52
Supported ops: subset of TFLite ops
RAM budget: as low as 16 KB
ONNX import via tf2onnx → tflite conversion
Micro-benchmark: 5 ms keyword spotting on nRF52
IDE: Arduino, PlatformIO, Keil MDK
Training: TensorFlow → TFLite → TFLM converter
Edge Impulse Platform:
Commercial platform (free tier available)
End-to-end: data capture → model → deploy
Supports: Arduino Nano 33 BLE, ESP32, Raspberry Pi
Auto quantization: FP32 → INT8 with accuracy report
Supports: classification, object detection, anomaly
Studio: no-code web interface for sensor data labeling
CLI: edge-impulse-cli for data ingestion from any device
Output: Arduino library or C++ SDK — drop into firmware
📚 Book-1, Ch.7, Pg 130-142

## Slide 20
Distributed IoT Data Processing with Apache Kafka
Production IoT systems need to handle millions of events per second from thousands of devices
Apache Kafka: distributed event streaming platform — the backbone of large-scale IoT data pipelines
Kafka architecture:
  Broker: Kafka server node that stores and serves messages
  Topic: named stream of events (e.g., 'factory.line1.temperature')
  Partition: horizontal sharding within topic — enables parallel consumption
  Consumer Group: set of consumers that each read a different partition — scales linearly
Throughput: 1 million messages/second per broker — handles the largest IoT deployments
Retention: messages kept for configurable period (1 hour to forever) — replay any time window
Kafka Streams: stream processing library — real-time aggregations, joins, windowed stats
  Example: 5-minute rolling average temperature across all factory sensors — pure stream processing
KSQL: SQL-like query language for Kafka streams
  'SELECT AVG(temp) FROM factory_sensors WINDOW TUMBLING (SIZE 5 MINUTES) GROUP BY machine_id'
Integration with IoT: MQTT Bridge → Kafka connector (MQTT Source Connector by Confluent) ingests MQTT topics into Kafka
At scale: AWS Managed Streaming for Kafka (MSK), Confluent Cloud, Redpanda (Kafka-compatible, 10× lower latency)
📚 Book-2, Ch.4, Pg 100-111

## Slide 21
05
Building the IoT Edge Infrastructure
📚 Book-2, Ch.4, Pg 100-111

## Slide 22
Node-RED: Visual Flow Programming for IoT Edge
Node-RED: open-source flow-based programming tool developed by IBM, donated to OpenJS Foundation
Runs on: Node.js — Raspberry Pi, Linux server, Docker, AWS Lambda, Azure IoT Edge
Core concept: connect 'nodes' with wires to build data flows — no traditional coding needed
Key node categories:
  Input nodes: MQTT subscriber, HTTP GET, Serial port, File reader, WebSocket
  Processing nodes: Function (custom JavaScript), Switch (routing), Change (transform), JSON parse
  Output nodes: MQTT publisher, HTTP POST, Email, Dashboard widget, InfluxDB write
  Dashboard nodes: gauge, chart, text, button — automatic web dashboard on port 1880/ui
Integration capabilities:
  REST API caller: make HTTP requests to any cloud API from a flow
  Modbus-TCP node: read industrial PLC registers directly into Node-RED flow
  node-red-contrib-influxdb: write time-series data to InfluxDB with one node
  node-red-contrib-tensorflow: run TFLite model inference inside a Node-RED flow
Installation: npm install -g node-red or runs in Docker container
Security: HTTPS + basic auth for production deployments; Projects mode for Git version control of flows
Why it matters: Node-RED is the most widely deployed IoT edge integration tool — 350K+ active installations
📚 Book-2, Ch.4, Pg 100-111

## Slide 23
Edge IoT Architecture with Node-RED + InfluxDB + Grafana
1
IoT Devices
ESP32/Raspberry Pi publish sensor JSON to MQTT broker on local network. No internet needed at this stage.
2
Node-RED (Edge)
Subscribes to MQTT topics. Parses JSON. Applies business rules. Filters noise. Triggers local alerts.
3
InfluxDB (Edge)
Time-series database receives processed readings from Node-RED. Stores 30 days locally with downsampling.
4
Grafana (Edge)
Visualization layer queries InfluxDB. Real-time dashboards. Alert rules. Accessible on local network.
5
Cloud Sync
Node-RED also forwards aggregated/summarized data to cloud (AWS IoT Core / Azure IoT Hub) asynchronously.
📚 Book-2, Ch.4, Pg 100-111

## Slide 24
LAB
Lab Session 3
📚 Node-RED + MQTT + Dashboard (no hardware required)

## Slide 25
LAB
Lab 3: Node-RED Edge Pipeline — Sensor Simulation to Dashboard
Tool: Node-RED (npm or Docker) + node-red-dashboard palette + paho-mqtt publisher from Lab 1
Install Node-RED locally:
Option A: npm install -g node-red → node-red (requires Node.js 18+)
Option B: docker run -it -p 1880:1880 nodered/node-red
→ Open browser: http://localhost:1880
Build the flow:
Part 1 — MQTT input:
→ Drag MQTT-in node → subscribe to 'iot/lab/sensor1' (from Lab 1 publisher)
→ Wire to JSON parse node → wire to Debug node → verify messages arriving
Part 2 — Processing:
→ Add Function node: extract temp, compute alert flag (temp > 35 = ALERT)
→ Add Switch node: route by alert flag → two branches
→ Branch 1 (normal): send to Dashboard gauge
→ Branch 2 (alert): send to Debug console + MQTT-out 'iot/alerts' topic
Part 3 — Dashboard:
→ Install via Manage Palette: node-red-dashboard
→ Add Gauge node (0–50°C range) + Chart node (last 30 readings)
→ Open http://localhost:1880/ui — live dashboard
Part 4 — InfluxDB writer (bonus):
→ Install node-red-contrib-influxdb
→ Write each reading to InfluxDB local instance
Submission: flow JSON export (copy from Node-RED → Export) + screenshot of dashboard

## Slide 26
Lab 3: Node-RED Function Node — Alert Logic (JavaScript)
JavaScript (Node-RED Function)
// Function node: 'Alert Logic'
// Input: msg.payload = { ts, temp_c, hum_pct }
// Output: same msg with alert flag added
const TEMP_HIGH = 35.0; // °C threshold
const TEMP_LOW = 10.0; // °C low threshold
const temp = msg.payload.temp_c;
const hum = msg.payload.hum_pct;
msg.payload.alert = temp > TEMP_HIGH ? 'HIGH_TEMP' :
temp < TEMP_LOW ? 'LOW_TEMP' : 'OK';
msg.payload.heatIndex = temp + 0.33 * (hum / 100 * 6.105 *
Math.exp(17.27 * temp / (237.7 + temp))) - 4.0;
// Add timestamp for InfluxDB
msg.payload.timestamp = new Date().toISOString();
// Route: output 1 = normal, output 2 = alert
if (msg.payload.alert !== 'OK') {
return [null, msg]; // alert branch
} else {
return [msg, null]; // normal branch
}

## Slide 27
Class 3 Recap
Key Takeaways
Edge computing moves processing near data source — solves latency (<10 ms), bandwidth (1000× reduction), reliability, and privacy
Three-tier edge: Tier 0 (MCU on-device) → Tier 1 (Raspberry Pi gateway) → Tier 2 (enterprise edge server)
Resource constraint triangle: Compute (240 MHz MCU) × Memory (256 KB–8 MB) × Energy (10 µA sleep) — must balance all three
Energy harvesting: solar, thermal (TEG), RF, piezoelectric enable zero-battery perpetual IoT nodes
TinyML: INT8 quantization + pruning + distillation enables ResNet-class accuracy on ARM Cortex-M MCUs
Federated Learning: gradient sharing (not raw data) trains global model across 1000s of edge devices — privacy-preserving AI
Swarm intelligence: decentralized, emergent collective behaviour (ACO, PSO, gossip protocols) for large device fleets
K3s + KubeEdge / AWS Greengrass: orchestrate containerized workloads across 100s of edge nodes at scale
Node-RED: visual flow programming — MQTT in → process → dashboard/alert/DB out; 350K+ deployments globally
Lab: Node-RED edge pipeline with MQTT input, alert routing, real-time dashboard (http://localhost:1880/ui)
Book-1: Springer Handbook of IoT (Ziegler, 2024) | Book-2: Hands-On Industrial IoT (Veneri, 2024)